## Slide 1: CS 107: Computer Architecture and Organization
SBCC
Fall 2019

## Slide 2
4 keystones of programming
- Assignment operator
MOV R2, #9
MUL R1, R0, R2 ; F = C * 9
MOV R2, #5
SDIV R1, R1, R2 ; F = (C * 9) / 5
MOV R2, #32
ADD R1, R1, R2 ; F = ((C * 9) / 5) + 32

## Slide 3
- Conditional operator
CMP R2, R7
SUBNE R2, R2, R7
ADDEQ R2, R2, R4
- Assignment operator
MOV R2, #9
MUL R1, R0, R2 ; F = C * 9
MOV R2, #5
SDIV R1, R1, R2 ; F = (C * 9) / 5
MOV R2, #32
ADD R1, R1, R2 ; F = ((C * 9) / 5) + 32
4 keystones of programming

## Slide 4
- Loop operator
loop_average
LDRH R5, [R3], #2 ; R5 = (*R3++); // Unsigned!
ADD R0, R0, R5 ; Average += R5
SUBS R1, #1 ; (Number of Elements)—
BNE loop_average ; if ( != 0) then loop...
UDIV R0, R0, R4 ; Average /= Number of elements
- Conditional operator
CMP R2, R7
SUBNE R2, R2, R7
ADDEQ R2, R2, R4
- Assignment operator
MOV R2, #9
MUL R1, R0, R2 ; F = C * 9
MOV R2, #5
SDIV R1, R1, R2 ; F = (C * 9) / 5
MOV R2, #32
ADD R1, R1, R2 ; F = ((C * 9) / 5) + 32
4 keystones of programming

## Slide 5
- Loop operator
loop_average
LDRH R5, [R3], #2 ; R5 = (*R3++); // Unsigned!
ADD R0, R0, R5 ; Average += R5
SUBS R1, #1 ; (Number of Elements)—
BNE loop_average ; if ( != 0) then loop...
UDIV R0, R0, R4 ; Average /= Number of elements
- Conditional operator
CMP R2, R7
SUBNE R2, R2, R7
ADDEQ R2, R2, R4
- Assignment operator
MOV R2, #9
MUL R1, R0, R2 ; F = C * 9
MOV R2, #5
SDIV R1, R1, R2 ; F = (C * 9) / 5
MOV R2, #32
ADD R1, R1, R2 ; F = ((C * 9) / 5) + 32
- Subroutine
???
4 keystones of programming

## Slide 6
Subroutine
sub- +‎ routine
Noun
subroutine (plural subroutines)
1.(computer science) A section of code, called by the main body of a program, that implements a task.
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0)
}

## Slide 7
sub- +‎ routine
Noun
subroutine (plural subroutines)
1.(computer science) A section of code, called by the main body of a program, that implements a task.
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0)
}
void main(void)
{
const byte str_1 = ‘HELLO’;
const byte str_2 = ‘CS 107’;
byte str_1_copy[8];
byte str_2_copy[8];
…
…
a = b + c;
str_copy(str_1, str_1_copy);
d = e + f;
…
…
k = i + m;
str_copy(str_2, str_2_copy);
…
}
Subroutine

## Slide 8
sub- +‎ routine
Noun
subroutine (plural subroutines)
1.(computer science) A section of code, called by the main body of a program, that implements a task.
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0)
}
void main(void)
{
const byte str_1 = ‘HELLO’;
const byte str_2 = ‘CS 107’;
byte str_1_copy[8];
byte str_2_copy[8];
…
…
a = b + c;
str_copy(str_1, str_1_copy);
d = e + f;
…
…
k = i + m;
str_copy(str_2, str_2_copy);
…
}
Subroutine

## Slide 9
sub- +‎ routine
Noun
subroutine (plural subroutines)
1.(computer science) A section of code, called by the main body of a program, that implements a task.
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0)
}
void main(void)
{
const byte str_1 = ‘HELLO’;
const byte str_2 = ‘CS 107’;
byte str_1_copy[8];
byte str_2_copy[8];
…
…
a = b + c;
str_copy(str_1, str_1_copy);
d = e + f;
…
…
k = i + m;
str_copy(str_2, str_2_copy);
…
}
Subroutine

## Slide 10
BL{CC} <label> ; LR = <addr of next instruction>
; PC = <label>
; or
; if (CC==true) {
; LR = <addr of next instruction>
; PC = <label>
; }
BX{CC} LR ; PC = LR or
; if (CC==true) PC = LR
LR = R14
Subroutine

## Slide 11
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
Subroutine

## Slide 12
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
Subroutine

## Slide 13
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000152
LR (R14) | …
R2 | 0x25252525
Subroutine

## Slide 14
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000164
LR (R14) | 0x00000157
R2 | 0x25252525
Subroutine

## Slide 15
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000172
LR (R14) | 0x00000157
R2 | 0x00000000
Subroutine

## Slide 16
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000156
LR (R14) | 0x00000157
R2 | 0x00000000
Subroutine

## Slide 17
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x0000015E
LR (R14) | 0x00000157
R2 | 0x52525252
Subroutine

## Slide 18
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000164
LR (R14) | 0x00000163
R2 | 0x52525252
Subroutine

## Slide 19
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000172
LR (R14) | 0x00000163
R2 | 0x00000000
Subroutine

## Slide 20
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
str_copy_loop
<0x00000164> LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000162
LR (R14) | 0x00000163
R2 | 0x00000000
Subroutine

## Slide 21
A stack is a container of objects that are inserted and removed according to the last-in first-out (LIFO) principle. In the pushdown stacks only two operations are allowed: push the item into the stack, and pop the item out of the stack. A stack is a limited access data structure - elements can be added and removed from the stack only at the top. push adds an item to the top of the stack, pop removes the item from the top. A helpful analogy is to think of a stack of books; you can remove only the top book, also you can add a new book on the top.
Subroutine

## Slide 22
Stack is placed in RAM.
May be as large as whole RAM.
General Purpose register(s) may be used as the stack pointer.
R13 (SP) is a dedicated register for stack pointer.
Stack may keep return addresses, local variables and parameters passed to subroutines.
May be used as temporary storage for any data.
PUSH{CC} {reg. list} ; Push
; R13 is SP
POP{CC} {reg. list} ; Pop
; R13 is SP
The {reg. list} list may contain any or all of R0 - R15
The lowest register always uses the lowest address, and so on, in increasing order
It doesn’t matter how the registers are ordered in {reg. list}
The example of {reg. list}:
  {R1, R2, R5-R8, LR}
  R1, R2, R5, R6, R7, R8 and LR are included
Subroutine

## Slide 23
PUSH {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000410
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0xFEFEFEFE
0x10000410 | 0xFEFEFEFE

## Slide 24
PUSH {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000404
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0xFEFEFEFE
0x10000410 | 0xFEFEFEFE
SP = SP – 3 * 4 ( SUB sp, #12 )
3 – number of registers in the list
4 – size of register in bytes (32 bits = 4 bytes)

## Slide 25
PUSH {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000404
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0x11111111
0x10000408 | 0xFEFEFEFE
0x1000040C | 0xFEFEFEFE
0x10000410 | 0xFEFEFEFE
SP = SP – 3 * 4
Mem[SP] = R1 ( STR r1, [sp] )

## Slide 26
PUSH {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000404
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0x11111111
0x10000408 | 0x55555555
0x1000040C | 0xFEFEFEFE
0x10000410 | 0xFEFEFEFE
SP = SP – 3 * 4
Mem[SP] = R1
Mem[SP + 4] = R5 ( STR r5, [sp, #4] )

## Slide 27
PUSH {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000404
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0x11111111
0x10000408 | 0x55555555
0x1000040C | 0x66666666
0x10000410 | 0xFEFEFEFE
SP = SP – 3 * 4
Mem[SP] = R1
Mem[SP + 4] = R5
Mem[SP + 8] = R6 ( STR r6, [sp, #8] )

## Slide 28
POP {R1, R5, R6}
Subroutine
R1 | 0x00000001
R5 | 0x00000005
R6 | 0x00000006
R13 (SP) | 0x10000404
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0x11111111
0x10000408 | 0x55555555
0x1000040C | 0x66666666
0x10000410 | 0xFEFEFEFE
R1 = Mem[SP]
R5 = Mem[SP + 4]
R6 = Mem[SP + 8]
SP = SP + 3 * 4

## Slide 29
POP {R1, R5, R6}
Subroutine
R1 | 0x11111111
R5 | 0x55555555
R6 | 0x66666666
R13 (SP) | 0x10000410
0x100003F4 | 0xFEFEFEFE
0x100003F8 | 0xFEFEFEFE
0x100003FC | 0xFEFEFEFE
0x10000400 | 0xFEFEFEFE
0x10000404 | 0x11111111
0x10000408 | 0x55555555
0x1000040C | 0x66666666
0x10000410 | 0xFEFEFEFE
R1 = Mem[SP]
R5 = Mem[SP + 4]
R6 = Mem[SP + 8]
SP = SP + 3 * 4

## Slide 30
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
<0x00000164> PUSH {R2}
str_copy_loop
LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
POP {R2}
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000164
LR (R14) | 0x00000157
SP (R13) | 0x10000410
R2 | 0x25252525
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0xFEFEFEFE
0x10000410 | 0x00000000
Subroutine
May be used as temporary storage for any data.

## Slide 31
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
<0x00000164> PUSH {R2}
str_copy_loop
LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
POP {R2}
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000166
LR (R14) | 0x00000157
SP (R13) | 0x1000040C
R2 | 0x25252525
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0x25252525
0x10000410 | 0x00000000
Subroutine
May be used as temporary storage for any data.

## Slide 32
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
<0x00000164> PUSH {R2}
str_copy_loop
LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
POP {R2}
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000174
LR (R14) | 0x00000157
SP (R13) | 0x1000040C
R2 | 0x00000000
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0x25252525
0x10000410 | 0x00000000
Subroutine
May be used as temporary storage for any data.

## Slide 33
void str_copy(byte *src, byte *dst)
{
char r2
do {
r2 = *src++;
*dst++ = r2;
} while (r2 != 0);
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
<0x00000164> PUSH {R2}
str_copy_loop
LDRB R2, [R0], #1 ; r2 = Mem[r0++]
STRB R2, [R1], #1 ; Mem[r1++] = r2
TEQ R2, #0 ; r2 == 0 ???
BNE str_copy_loop ; while (r2 != 0)
POP {R2}
BX LR ; return
MOV R2, #0x25252525
LDR R0, =str_1
LDR R1, =str_1_copy
<0x00000152> BL str_copy (0x00000164)
<0x00000156> MOV R2, #0x52525252
LDR R0, =str_2
LDR R1, =str_2_copy
<0x0000015E> BL str_copy (0x00000164)
stop
<0x00000162> B stop
PC (R15) | 0x00000176
LR (R14) | 0x00000157
SP (R13) | 0x10000410
R2 | 0x25252525
0x10000404 | 0xFEFEFEFE
0x10000408 | 0xFEFEFEFE
0x1000040C | 0x25252525
0x10000410 | 0x00000000
Subroutine
May be used as temporary storage for any data.

## Slide 34
void str_copy(byte *src, byte *dst)
{
char r3
long r2 = str_size(src);
do {
r3 = *src++;
*dst++ = r3;
r2--;
} while (r2 > 0);
}
function str_size(byte *r0)
{
long r2 = 0
do {
r3 = *r0++
r2++
} while (r3 != 0);
return r2;
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
BL str_size ; r2 = str_size(r0)
str_copy_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
STRB R3, [R1], #1 ; Mem[r1++] = r3
SUBS R2, #1 ; r2—
BGT str_copy_loop ; while (r2 > 0)
BX LR ; return
str_size
; R0 - source address (input)
; R2 - length of the string (result)
; R3 - temporary variable
MOV R2, #0 ; Result := 0
str_size_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
ADD R2, R2, #1 ; r2++
TEQ R3, #0 ; r3 == 0 ???
BNE str_size_loop ; while (r3 != 0)
BX LR ; return
Subroutine

## Slide 35
void str_copy(byte *src, byte *dst)
{
char r3
long r2 = str_size(src);
do {
r3 = *src++;
*dst++ = r3;
r2--;
} while (r2 > 0);
}
function str_size(long r0)
{
long r2 = 0
do {
r3 = *r0++
r2++
} while (r3 != 0);
return r2;
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
BL str_size ; r2 = str_size(r0)
str_copy_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
STRB R3, [R1], #1 ; Mem[r1++] = r3
SUBS R2, #1 ; r2—
BGT str_copy_loop ; while (r2 > 0)
BX LR ; return
str_size
; R0 - source address (input)
; R2 - length of the string (result)
; R3 - temporary variable
MOV R2, #0 ; Result := 0
str_size_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
ADD R2, R2, #1 ; r2++
TEQ R3, #0 ; r3 == 0 ???
BNE str_size_loop ; while (r3 != 0)
BX LR ; return
Lost Source Address!
Lost LR!
Subroutine

## Slide 36
void str_copy(byte *src, byte *dst)
{
char r3
long r2 = str_size(src);
do {
r3 = *src++;
*dst++ = r3;
r2--;
} while (r2 > 0);
}
function str_size(long r0)
{
long r2 = 0
do {
r3 = *r0++
r2++
} while (r3 != 0);
return r2;
}
str_copy
; R0 - source address
; R1 - destination address
; R2 - temporary variable
PUSH {R2, R3, LR} ; save r2, r3 and LR
BL str_size ; r2 = str_size(r0)
str_copy_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
STRB R3, [R1], #1 ; Mem[r1++] = r3
SUBS R2, #1 ; r2—
BGT str_copy_loop ; while (r2 > 0)
POP {R2, R3, PC} ; restore registers and
; return LR -> PC
;
BX LR ; return
str_size
; R0 - source address (input)
; R2 - length of the string (result)
; R3 - temporary variable
PUSH {R0, R3} ; save registers r0 and r3
MOV R2, #0 ; Result := 0
str_size_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
ADD R2, R2, #1 ; r2++
TEQ R3, #0 ; r3 == 0 ???
BNE str_size_loop ; while (r3 != 0)
POP {R0, R3} ; restore r0 and r3
BX LR ; return
Subroutine
Stack may keep return addresses…

## Slide 37
Passing parameters and results
CS 107 - Computer Architecture and Organization.
The organization and behavior of real computer systems at the assembly-language level. The mapping of statements and constructs in a high-level language into sequences of machine instructions is studied, as well as the internal representation of simple data types, pointers, structures, and non-numeric data. Numerical computation is also examined.
Subroutine

## Slide 38
Passing parameters and results
General registers.
Subroutine

## Slide 39
Passing parameters and results
General registers.
str_copy
; R0 - source address (input)
; R1 - destination address (input)
; R2 - temporary variable
PUSH {R2, R3, LR} ; save r2, r3 and LR
BL str_size ; r2 = str_size(r0)
str_copy_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
STRB R3, [R1], #1 ; Mem[r1++] = r3
SUBS R2, #1 ; r2—
BGT str_copy_loop ; while (r2 > 0)
POP {R2, R3, PC} ; restore registers and
; return LR -> PC
;
str_size
; R0 - source address (input)
; R2 - length of the string (result)
; R3 - temporary variable
PUSH {R0, R3} ; save registers r0 and r3
MOV R2, #0 ; Result := 0
str_size_loop
LDRB R3, [R0], #1 ; r3 = Mem[r0++]
ADD R2, R2, #1 ; r2++
TEQ R3, #0 ; r3 == 0 ???
BNE str_size_loop ; while (r3 != 0)
POP {R0, R3} ; restore r0 and r3
BX LR ; return
Subroutine

## Slide 40
Passing parameters and results
General registers.
Common variables.
Subroutine

## Slide 41
Passing parameters and results
General registers.
Common variables.
LDR R1, =A ; Save 2 into var A
MOV R2, #2
STR R2, [R1]
MOV R2, #3 ; Save 3 into var B
STR R2, [R1, #4]
BL sub_add ; Call subroutine
LDR R1, =C ; Read result from var C
LDR R2, [R1] ; into R2
. . .
sub_add
PUSH {R5, R6, R7, LR} ; Save registers
LDR R5, =A ; R6 = A + B
LDR R6, [R5], #4
LDR R7, [R5], #4
ADD R6, R7
STR R6, [R5] ; Save result (R6) to var C
. . .
POP {R5, R6, R7, PC} ; Restore regs. and return
AREA variables, DATA, ALIGN=2
A
SPACE 4
B
SPACE 4
C
SPACE 4
Subroutine

## Slide 42
Passing parameters and results
General registers.
Common variables.
Stack
Subroutine

## Slide 43
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | 
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 44
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | First parameter
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 45
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | Second parameter
 | First parameter
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 46
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | Third parameter
 | Second parameter
 | First parameter
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 47
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | Third parameter
 | Second parameter
 | First parameter
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 48
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
. . .
 | 0xfefefefe
 | 0xfefefefe
SP | R3
 | R4
 | R5
 | LR
 | Third parameter
 | Second parameter
 | First parameter
Subroutine
Stack may keep … parameters passed to subroutines.

## Slide 49
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
. . .
 | 0xfefefefe
 | 0xfefefefe
SP | R3
SP+4 | R4
SP+8 | R5
SP+12 | LR
SP+16 | Third parameter
SP+20 | Second parameter
SP+24 | First parameter
Stack may keep … parameters passed to subroutines.
Subroutine

## Slide 50
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
 | 0xfefefefe
 | 0xfefefefe
SP | R3
SP+4 | R4
SP+8 | R5
SP+12 | LR
SP+16 | Third parameter
SP+20 | Second parameter
SP+24 | First parameter
Subroutine

## Slide 51
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, PC} ; restore registers
; and return
 | 0xfefefefe
 | 0xfefefefe
SP | R3
SP+4 | R4
SP+8 | R5
SP+12 | LR
SP+16 | Third parameter
SP+20 | Second parameter
SP+24 | First parameter
Subroutine

## Slide 52
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, PC} ; restore registers
; and return
 | 0xfefefefe
 | 0xfefefefe
SP | R3
SP+4 | R4
SP+8 | R5
SP+12 | LR
SP+16 | Third parameter
SP+20 | Second parameter
SP+24 | First parameter
Subroutine

## Slide 53
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, PC} ; restore registers
; and return
 | 0xfefefefe
 | 0xfefefefe
 | R3
 | R4
 | R5
 | LR
SP | Third parameter
 | Second parameter
 | First parameter
Subroutine

## Slide 54
Stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
ADD SP, #12 ; Clear stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs. and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, PC} ; restore registers
; and return
 | 0xfefefefe
 | 0xfefefefe
 | R3
 | R4
 | R5
 | LR
 | Third parameter
 | Second parameter
 | First parameter
SP | 
Subroutine

## Slide 55
Stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs.
; and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, PC} ; restore registers
; and return
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; r0 = p1 + p2 + p3
; return r0
; }
; r0 - result
; r3, r4, r5 - temporary variables
;
PUSH {R3-R5, LR} ; save temp. var. regs.
; and LR
LDR R3, [SP, #24] ; First parameter
LDR R4, [SP, #20] ; Second parameter
LDR R5, [SP, #16] ; Third parameter
ADD R0, R3, R4 ; r0 = p1 + p2
ADD R0, R5 ; r0 = r0 + p3
POP {R3-R5, LR} ; restore registers
ADD SP, #12 ; Clear stack
BX LR ; return
Subroutine

## Slide 56
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | Third parameter
 | Second parameter
 | First parameter
Subroutine

## Slide 57
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
 | 0xfefefefe
SP | R3
 | R4
 | R5
 | LR
 | Third parameter
 | Second parameter
 | First parameter
Subroutine

## Slide 58
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
SP | C (0xfefefefe)
SP+4 | B (0xfefefefe)
SP+8 | A (0xfefefefe)
SP+12 | R3
SP+16 | R4
SP+20 | R5
SP+24 | LR
SP+28 | Third parameter
SP+32 | Second parameter
SP+36 | First parameter
Subroutine

## Slide 59
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
SP | C (0xfefefefe)
SP+4 | B (0xfefefefe)
SP+8 | A (0x66666666)
SP+12 | R3
SP+16 | R4
SP+20 | R5
SP+24 | LR
SP+28 | Third parameter
SP+32 | Second parameter
SP+36 | First parameter
Subroutine

## Slide 60
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
 | C (0xfefefefe)
 | B (0xfefefefe)
 | A (0x66666666)
SP | R3
 | R4
 | R5
 | LR
 | Third parameter
 | Second parameter
 | First parameter
Subroutine

## Slide 61
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
 | C (0xfefefefe)
 | B (0xfefefefe)
 | A (0x66666666)
 | R3
 | R4
 | R5
 | LR
SP | Third parameter
 | Second parameter
 | First parameter
Subroutine

## Slide 62
Local variables on stack
MOV R0, #0x11111111 ; First parameter
PUSH {R0}
MOV R0, #0x22222222 ; Second parameter
PUSH {R0}
MOV R0, #0x33333333 ; Third parameter
PUSH {R0}
BL sub_stack
. . .
sub_stack
; func sub_stack(long p1, long p2, long p3)
; {
; var long a, b, c
; a = p1 + p2 + p3
; . . .
; r0 = b
; return r0
; }
PUSH {R3-R5, LR} ; save temp. var. registers.
SUB SP, #12 ; Allocate a, b, c
LDR R3, [SP, #36] ; First parameter
LDR R4, [SP, #32] ; Second parameter
LDR R5, [SP, #28] ; Third parameter
ADD R3, R3, R4 ; r3 = p1 + p2
ADD R3, R5 ; r3 = r0 + p3
STR R3, [SP, #8] ; a = p1 + p2 + p3
; . . .
LDR R0, [SP, #4] ; r0 = b
ADD SP, #12 ; Destroy a, b, c
POP {R3-R5, LR} ; restore temp. registers
ADD SP, #12 ; Clear stack
BX LR ; return
 | 0xfefefefe
 | 0xfefefefe
 | C (0xfefefefe)
 | B (0xfefefefe)
 | A (0x66666666)
 | R3
 | R4
 | R5
 | LR
 | Third parameter
 | Second parameter
 | First parameter
SP | 
Subroutine

## Slide 63
Subroutine
LAB 6
Subroutines
(Based on Lab2-Lab5)